## Slide 1: R R Proctor
During the construction of Bouquet Canyon Dam (1932 to 1934),
developed what we now call the "Proctor-test", to determine the optimum water content of the compacted earth fill used for the dam core construction.

## Slide 2: Proctor Curve
Zero air voids line
ZAV
Dry Density
Moisture content
d max
OMC
Soil too dry and brittle
Soil too wet & deformable
The aim of the test is to establish the maximum dry density that may be attained for a given soil with a standard amount of compactive effort. When a series of samples of a soil are compacted at different water content the plot usually shows a distinct peak.

## Slide 3: Compaction Mechanism
Compaction (concept): the densification of soil by removal of air. Requires mechanical energy Densification increases with help of water.
water acts as softening agent and allows soil particles to slip over one another thereby increasing the packing factor

## Slide 4: Factors Affecting The Compaction
Factors | Control
Nature and type of soil, i.e. sand or clay, grading, plasticity | No Control. Depends on material availability
Water content at the time of compaction | Controllable
Site conditions, e.g. weather, type of site, layer thickness | Controllable by choosing proper combination of equipment and lift thickness
Compactive effort | Controllable by choosing proper combination of equipment and lift thickness

## Slide 5: Laboratory Compaction Tests
Standard Proctor Test: -
  mould 4.6” * 4” diameter
  hammer weight = 5.5 Ib
  height of hammer drop = 12”
  No. of blows/layer = 25 No. of layers = 3
Modified Proctor Test: -
  mould 4.6” * 4” diameter
  hammer weight = 10 Ib
  height of hammer drop = 18”
  No. of blows/layer = 25
  No. of layers = 5
Modified proctor is: -
  more hammer weight
  more hammer drop distance
  more no. of layers

## Slide 6: Role of Compactive Effort
The compactive effort will be greater when using a heavier roller on site or a heavier rammer in the laboratory. With greater compactive effort:
  maximum dry density increases
  optimum water content decreases
  air-voids content remains almost the same.
Dry Density
Moisture content
Standard Compaction
Modified Compaction

## Slide 7: Compactive Effort
Smoothed drum Roller | 20 psi to 50 psi
Sheep's Foot Roller | 175 psi to 700 PSI

## Slide 8: Can We design Soil Compaction?
Yes
“Mathematical Approach to Simulate Soil Behavior under Shallow Compaction” by Ahmed M .Ebid

## Slide 9: Parameter for Soil Compaction design
B= Contact width For rigid rollers, using modified Grecenko formula as follows: B = (0.45 - 0.15 γ) x Roller diameter
F= is the fines percent (Soil Passing #200 sieve)
=Dry Unit Weight of Soil Tons/cum
= stress at ground surface

## Slide 10: Proposed Procedure for Soil Compaction Design ?
The proposed approach depends on calculating the lift settlement after each pass considering the fact that only effective depth is affected by compaction effort
accordingly fill proprieties will be updated to be used to calculate the settlement of the next pass.
Pass after pass, the effective depth decreases due to ultimate bearing capacity enhancing until it equal to zero when the ultimate bearing capacity exceeds the effective contact stress,
at this time, the dry density reaches its maximum value and any mare passes will not have any effect on the soil.

## Slide 11: Computer Program for Soil Compaction Design?
This is an iterative procedure can be programmed.

## Slide 12: Moisture Content Measurement – Moisture Analyzer

## Slide 13: Moisture Content Measurement – Electronics sensor